## Slide 1: Unconventional Oil and Gas Plays: Berea Sandstone and Rogersville Shale
Dave Harris
Energy and Minerals
Section
May 13, 2016

## Slide 2: What’s an Unconventional Reservoir?
Low-permeability rock or heavy oil (shale, tight ss, coal)
Source rock = reservoir
Special technology required to produce hydrocarbons at economic rates
Not new: production in Kentucky for decades
Nano-scale porosity in shale,
(courtesy of FEI)

## Slide 3: Unconventional Revolution
Large reserves
High pressure
Lower risk

## Slide 4: New Unconventional Plays
Upper Devonian Berea Sandstone
  Greenup, Lawrence Counties, northeastern Ky.
  Active horizontal oil play since 2011
  Low-volume hydraulic fracture stimulations
  Very shallow depth (700-1,600 ft)
Berea Sandstone
Outcrop, Lewis County
(photo: Steve Greb)

## Slide 5
Cambrian Rogersville Shale
  Deep Rome Trough
  Lawrence and Johnson Counties, eastern Ky.
  Early appraisal phase (most data confidential), gas and oil
  9,000 to 14,000 ft deep
  High-volume hydraulic fracture stimulation

## Slide 6: Berea Sandstone
Upper Devonian marine shelf siltstone/ very fine sandstone
Avg. porosity (~13%) and permeability (2.2 md)
Encased by Sunbury and Ohio Sh, both organic-rich shales

## Slide 7
New oil play in older producing area (horizontal infill)
“Tight sand”- very fine sandstone to siltstone; low permeability
Key technology: horizontal drilling with hydraulic fracturing (ave. 252,000 gal fluid)
Shallow depth: 700–1,600 ft
Production rates of 20-200 barrels/day reported
Horizontal Oil Play in the Berea Sandstone

## Slide 8: 2015 Oil Production: 2.8 MMbo
Chart: Million Barrels
| 1981 | 1982 | 1983 | 1984 | 1985 | 1986 | 1987 | 1988 | 1989 | 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007 | 2008 | 2009 | 2010 | 2011 | 2012 | 2013 | 2014 | 2015
OilMMbo | 6.4895 | 7.3437 | 7.9759 | 7.7972 | 7.7843 | 6.4834 | 5.7534 | 5.4404 | 5.3282 | 5.3485 | 5.4881 | 5.3817 | 4.5926 | 4.1031 | 3.5604 | 3.4481 | 2.9387 | 3.0017 | 2.8076 | 2.8739 | 2.7981 | 2.7209 | 2.5379 | 2.5481 | 2.4539 | 2.1708 | 2.6177 | 2.616 | 2.5524 | 2.5194 | 2.3259 | 3.198 | 2.959 | 4.07 | 2.854
58 %
34.2 %
8.3 %
(2014 – 75% increase over 2011)
63 Kentucky counties
Slide credit: Brandon Nuttall
Notes: Horizontal oil wells drilled in northeast Kentucky beginning in 2011 pushed annual production to more than 4 million barrels in 2014, the highest production since 1994. In 2015, production fell 30% to 2.8 million barrels. Eastern Kentucky produces 58% of the statewide total oil.

## Slide 9: Cambrian Rogersville Shale (Conasauga Group)
KGS identified hydrocarbon source potential in 2002 Rome Trough Consortium study
Source for Elliott County, Ky. Homer Field gas and oil
2-4.8% total organic carbon in parts; thermally mature
5,000 to 10,000 ft deep in E. Ky.
Up to 1,100 ft thick, but limited to deeper parts of Rome Trough (and not all is organic-rich)

## Slide 10: Rogersville Shale Wayne Co., W. Va. 11,191-11,200’

## Slide 11
Chesapeake LAW1 Northup Est
Bruin Expl 1 Walbridge
Hard Rock Expl 1 Young, GD
Cabot 50 Amherst Industries
Chesapeake LAW1 Stephens, J
Bruin Expl 1 Young, S
Horiz. Tech Energy 572360 EQT
Play concept proven, economics are not

## Slide 12: Impacts
Significant increase in state oil production from Berea; too early for Rogersville
New regulations for unconventional wells:
  High-volume horizontal fracs: >80,000 gal per stage or 320,000 gal total
  For deep HVHF: notify surface owners before frac, and surface water/groundwater testing required
  FracFocus disclosure required for HVHF within 90 days
KGS research to support prudent development

## Slide 13: KGS Research Response
Industry-funded Berea Consortium just completed 21-month multidisciplinary study
Two new research programs to collect baseline data:
  Microseismic: Seth Carpenter, Hazards Section
  Groundwater quality: Junfeng Zhu, Water Section
Pre-development baseline data will allow recognition of natural vs. man-made events
Goal: avoid induced seismicity and other energy development-related issues